## Slide 1: Two routes towards fibre-integrated optical switching with single photons
Cameron McGarry
The University of Bath, United Kingdom
SPIE Photonics West, San Francisco
28th January 2024

## Slide 2
Pete Mosley
Tim Birks
Kristina Rusimova
Kerrianne Harrington
Josh Nunn
Centre for Photonics and
Photonic Materials
Tabijah Wasawo
Will Davis

## Slide 3: Quantum technology
Bit (binary digit) → qubit (quantum binary digit)
Exploit quantum resources (superpositions, entangled states, etc.)
Promises improvements in:
  Precision measurement
  Tests of fundamental physics
  Encryption & decryption
  Drug discovery
  Material development
  Machine learning
  Quantum chemistry
  Whatever else you need to please your funding body

## Slide 4: Photons are great for quantum tech
Encoding (e.g. in polarisation)
Low interaction with environment (low decoherence)
High bandwidth (flying qubits)
Readily confined to waveguides (inc. optical fibre)

## Slide 5: How do you store a photon?

## Slide 6: How do you store a photon?
Ran Finkelstein et al. Fast, noise-free memory for photon synchronization at room temperature. Sci. Adv. 4, (2018). DOI:10.1126/sciadv.aap8598
Fast ladder memory (FLAME)

## Slide 7: FLAME: a memory, but with limited efficiency
Ran Finkelstein et al. Fast, noise-free memory for photon synchronization at room temperature. Sci. Adv. 4 (2018). DOI:10.1126/sciadv.aap8598
Davidson, O., Yogev, O., Poem, E. et al. Fast, noise-free atomic optical memory with 35-percent end-to-end efficiency. Commun Phys 6, 131 (2023). https://doi.org/10.1038/s42005-023-01247-4
Efficiency: 32(1)%
Storage time: 86(2) ns
Photon noise: 5.8(4) × 10-5
Recent improved memory
Efficiency: 39.8(6)%
Storage time: 113(2) ns
Photon noise: 1.2(2) × 10-5

## Slide 8: How do you store a photon?
Loop memory

## Slide 9: How do you store a photon?
Loop memory
Switch

## Slide 10: How do you store a photon?
Loop memory
Switch

## Slide 11: How do you store a photon?
Loop memory
Switch requirements:
Fast
Low-loss
Switch

## Slide 12: How do you store a photon?
Switch requirements:
Fast
Low-loss
How do you switch a photon?

## Slide 13: How do you store a photon?
Switch requirements:
Fast
Low-loss
How do you switch a photon?

## Slide 14: How do you store a photon?
How do you switch a photon?
How do you phase modulate a photon?

## Slide 15: What’s my FLAME again?
Ran Finkelstein et al. Fast, noise-free memory for photon synchronization at room temperature.Sci. Adv.4,eaap8598(2018). DOI:10.1126/sciadv.aap8598
Fast ladder memory (FLAME)

## Slide 16: All-optical phase modulation
Control field on/off changes susceptibility
Hence introduces phase shift

## Slide 17: All-optical phase modulation

## Slide 18: All-optical phase modulation

## Slide 19: All-optical phase modulation: results

## Slide 20: Phase modulation back to optical memory
Phase modulation
Port switching
Quantum memory

## Slide 21: All-optical switching mediated by Rb
Arxiv: 2309.04313

## Slide 22: How do you store a photon?
Realise directly with a cavity
How do you switch a photon?
Vapour cell
Signal input
Transmitted output
Reflected output

## Slide 23: Cavity-integrated optical switch
Control field changes susceptibility as before
Effectively changing refractive index of cavity
Rapid switch of cavity from strong transmission to strong reflection
Vapour cell
Signal input
Transmitted output
Reflected output

## Slide 24: Cavity-integrated optical switch: results
Vapour cell
Signal input
Transmitted output
Reflected output

## Slide 25: Cavity-integrated optical switch: future
Lock lasers off-resonance for high transmission
Rapid switching with EOM to modulate control field

## Slide 26: Miniaturisation: in-fibre vapour cell
Atoms inside a hollow core fibre
Low-loss interconnections via GIF lens

## Slide 27: Low-loss fibre interconnects
Device insertion loss 0.6(2) dB at 780 nm
Mode matching with GIF lens
HCF loss given over 50cm (cell length)

## Slide 28: Low-loss, fibre-integrated vapour cell
Arxiv: 2401.10651

## Slide 29: Future work
Port-switching in a cavity
Phase modulation at telecoms wavelengths
Fill fibre cell with Rb

## Slide 30: Thank you

## Slide 31: Emergency slides

## Slide 32: Exactly one slide about hollow core optical fibre (HCF)
Cladding
25 μm
Stray light in resonator
Light guided
in core
Core
Resonator
Jacket
SMF
HCF
HCF

## Slide 33: How to fabricate fibre

## Slide 34: Cleave GRIN to length with customised tension cleaver

## Slide 35: Previous work
Big macroscopic cold splices (or no loss reported)
Not encapsulated
Telecoms wavelengths
Dmytro Suslov et al All-fiber hollow-core fiber gas cell. Optical Fiber Technology, Vol 81 (2023). DOI:10.1016//j.yofte.2023.1035113

## Slide 36: A robust splice inside a capillary

## Slide 37: Mode matching with a GRIN lens

## Slide 38: Mode matching with a GRIN lens
L

## Slide 39: Mode matching with a GRIN lens
50 μm

## Slide 40: Cut back experiment

## Slide 41: Results: cutback and measure loss

## Slide 42: Results: high resolution reveals beating

## Slide 43: Results: near wavelength of interest

## Slide 44: Multiple modes in the HCF
Testing different HCF lengths

## Slide 45: Multiple modes in the HCF
Testing different HCF lengths

## Slide 46: Phase matching to optimise transmission

## Slide 47: AR coating improvements